Paul Huddlestun

3-73

11/4/11

GEORGIA POWER CORE B-33

SCREVEN COUNTY, GEORGIA

Burtons Ferry Landing 7½’ Quadrangle

On the side of Old River Road,

Approximately 1.8 miles north of jct. of Old River Road and US 301

In eastern Screven County, GA

Latitude		32°°57.475’                       Elev. 115 Feet

Longitude		81° 32.484’

N 1,077,625

E 691,510

Lithostratigraphic

unit and bed number                          Description                 Thickness      Depth

(feet           (feet)

NO CORE                                                                                       5.0              0.0

Bed 1		Chert:  fossiliferous; indurated; ~22% net                  8.0              5.0

recovery; overlies core gap:

NO CORE 	               “split spoon, no recovery”                            9.0             13.0

UPPER EOCENE, LOWER JACKSONIAN

BARNWELL GROUP

DRY BRANCH FORMATION – 42 feet+ thick

Griffins Landing Member

Bed 2		Limestone: sandy, slightly argillaceous;                  3O.0            108.0

medium to course textured, calcarenitic;

slightly consolidated in upper part, soft and

unconsolidated in lower part; almost 	a

coquina of small, branching bryozoans in the

upper part, common foraminifera; core gap

between ~128 feet and ~133 feet; moderately

to poorly competent (~39% core recovery);

abruptly overlies (contact between cores):

Twiggs lithofacies – 12 feet

Bed 3		Clay: silty, micaceous, calcareous, some                 12.0            138.0

thin layers of sandy limestone or calcareous

sandstone, some thin beds or laminae or

fine sand interlayered with clay; thinly

bedded to laminated, shaley when dry;

mostly competent (~97% core recovery);

gradationally overlies:

UPPER EOCENE?/MIDDLE EOCENE?

BARNWELL GROUP

CLINCHFIELD FORMATION – 25 feet thick

Utley Limestone Member

Bed 4		Calcareous sandstone to sandy limestone:                3.0            150.0

coarse and rubbly textured, calcarenitic,

bioclastic; some fine grained, dense sandstone

and bits of shaley clay: macrofossiliferous;

moderately competent (~60% core recovery);

overlies core gap:

VERY POOR RECOVERY

“some fine dense sandstone and bits of                  10.0            153.0

shaley clay”

Bed 4		Limestone:  sandy, glauconitic, fossiliferous;          12.0            163.0

even textured and moldic in upper part,

rubbly, poorly sorted and bioclastic in lower

part; massive bedded and structureless;

indurated; abruptly overlies:

MIDDLE EOCENE, CLAIBORNIAN

UNNAMED CLAIBORNIAN LIMESTONE – 87.5 feet thick

Blue Bluff-equivalent

Bed 5		Limestone: much pelletal, granular,                        87.5            175.0

equidimensional, calcitic, bioclastic material,

moderately poor sorting, conspicuous

calcilutitic matrix, 	calcarenite is generally

even textured, medium grained and rubbly in

the upper part, texture becomes more even,

less rubbly, and poorly sorted in the lower

part; a one foot bed of bioclastic, coarsely

shelly (oysters and scallops) limestone occurs

at ~208 feet; a trace of glauconite, glauconite

content increases downward with the

introduction of clay below about ~210 feet,

very minor clay in the lower part; core

appears to be massive and structureless

but Bed 5 is probably thickly and rudely

bedded, resulting from the alternation of

indurated limestone (most of the limestone

is indurated) with unconsolidated limestone

and, possibly, the presence of scattered

fossiliferous lenses; mostly competent

(~97% core recovery); abruptly but

gradationally overlies:

CLAIBORNE GROUP

LISBON FORMATION – 10.7 feet thick+

probably Blue Bluff Member? or pre--Blue Bluff?

Bed 6		Clay: very calcareous, silty to finely sandy,             10.7            262.5

micaceous and sparsely glauconitic; massive

bedded and structureless; moderately

competent (~43% core recovery); bottom of

core at 273,5 feet.

____________________________                                                                                  TOTAL DEPTH – 273.2 FEET

Core has been disposed of in 1973/1974