Paul Huddlestun

Logged ca. 1976

Written up – 11/1/14

WASHINGTON 17 (HARRISON CORE), GGS-1189

WASHINGTON COUNTY, GEORGIA

Harrison 7½’ Quadrangle

Approximately 1.1 miles east of Harrison, Washington County,

on the western shoulder of GA HWY 231 (Harrison Riddleville Road), and

0.6 miles northeast of the jct. of GA HWY 231 and Harrison Pringle Road

Latitude		N 32° 49.817’                             Elev. 412 feet

Longitude        W 82° 42.484’

Lithostratigraphic

unit and bed number               Description                     Thickness          Depth __________________________________________________________(feet)__________(feet)

SOIL

Bed 1		Sand: medium grained and moderately well           1.5               0.0

sorted; no other lithic components noted;

structureless; unconsolidated, soft and poorly

coherent; abruptly overlies:

MIOCENE (LOWER?), AQUITANIAN?

ALTAMAHA FORMATION – 60 feet

Bed 2		Clay: finely sandy in the upper part with sand        48.5             1.5

content gradually diminishing down-section;

a thin, 6 inch layer of claystone noted at 44.25

feet, the cementing agent unknown but is

probably silica; no other lithic components

noted; massive and structureless; very tough

and resistant yet unconsolidated (except for

the claystone) and competent (˃100% core

recovery); deeply weathered; grades

downward by increasing fine sand content

into:

Bed 3		Clay: slightly and finely sandy in the upper            9.0             50.0

part of the Bed with the sand content

increasing gradually downward; massive and

structureless; tough and resistant but

unconsolidated, mostly competent (~78% core

recovery); grades downward by increase in

clay content into:

Bed 4		Clay: finely sandy and silty; the lower part is        0.5             59.0

slightly indurated, being transitional to the

underlying sandstone/claystone;

structureless; partially but somewhat

indurated and competent; weathered; grades

downward into:

Bed 5		Sandstone/claystone (characteristic Altamaha       2.0             59.5 		sandstone/claystone): fine to coarse grained

and poorly sorted, pebbly in the lower part of

the Bed; argillaceous to clayey; massive and

structureless; indurated, friable and

competent; appears to be unweathered,

yellowish gray (5Y 8/1) in color; abruptly and

disconformably overlies:

UPPER EOCENE, UPPER JACKSONIAN

BARNWELL GROUP

TOBACCO ROAD SAND – 27.5 feet

Bed 6		Clay: finely sandy to silty and well sorted,              9.5             61.5

becoming more sandy down-section;	scattered

feldspar grains; thinly layered; unconsolidated

but competent (100% core recovery); light

olive gray (5GY 6/1) in the upper part,

shading to grayish yellow green (5GY 7/2) in

the lower part of the Bed; grades downward

by gradual increase in sand content and

sand-size into:

Bed 7		Clayey sand/sandy clay: sand is fine/medium       8.0             71.0

to fine grained and well sorted; clay occurs

interstitially, somewhat micaceous and a trace

of MnO2 in the clayey or thin layers; thinly

stratified; unconsolidated, coherent and

competent (˃100% core recovery); the color

ranges around greenish gray to grayish yellow

green (5GY 6/1 to 5GY 7/2); grades

downward by diminishing clay content into:

Bed 8		Sand: medium grained and well sorted; clayey        9.0             79.0

matrix; massive and structureless;

unconsolidated but tough and competent

(˃100% core recovery); pale to very pale

greenish yellow green (5GY 8/2 – 5GY 9/2) in

color; grades downward into:

Bed 9		Sand: coarse grained and poorly sorted, some        1.0             88.0

very coarse grains and granules; argillaceous

and feldspathic; vaguely and rudely stratified;

very tough and competent but not indurated

(˃100% core recovery); abruptly overlies:

UPPER EOCENE, LOWER JACKSONIAN

BARNWELL GROUP

DRY BRANCH FORMATI0N

Irwinton Sand Member – 16 feet+

Bed 10	Sand: fine to fine/medium grained and well         13.0             89.0

sorted; argillaceous with interstitial clay, clay

content decreases downward, clayey texture

in the upper part of the Bed; prominently

stratified; unconsolidated but rather tough

and competent (˃100% core recovery); grayish

yellow green to light greenish gray (5GY 7/2 –

5GY 8/1) in color; grades downward into:

Bed 11	Sand: fine grained and well sorted; somewhat       3.0            102.0

argillaceous with both interstitial clay and

clay in thin layers and laminae; prominently

stratified; unconsolidated and mostly coherent

and competent (˃87% core recovery) light

grayish yellow green to light grayish green

(5GY 8/2 – 5GY 8/1) in color; bottom of the

core at 105 feet.

_______________________________________

TOTAL DEPTH OF CORE – 105.0 FEET