Paul Huddlestun

Logged ca. 1976

Written up – 10/25/14

WASHINGTON (RIDDLEVILLE CORE), 8a, GGS-1180

WASHINGTON COUNTY, GEORGIA

Riddleville 7½’ quadrangle

0.5 miles mile west of Riddleville,

on the shoulder of GA HWY 242 (Bartow Road),

less than 0.1 mile east of the jct. of Bartow Road and

South Riddle Road

Latitude		N 32° 54.901’                            Elev. 393 Feet

Longitude        W 82° 41.017’

Lithostratigraphic

unit and bed number               Description                     Thickness          Depth  __________________________________________________________(feet)_________ (feet)

NO CORE TAKEN IN UPPER 60 FEET                                      60.0              0.0

THE TOP OF CORE 8a OCCRS AT A DEPTH OF

99 FEET IN THE NEARBY CORE WASHINGTON 8

UPPER EOCENE, UPPER JACKSONIAN?

BARNWELL GROUP

TOBACCO ROAD SAND? – 4.0 feet

Bed 1		Sand: medium grained and well sorted;                  4.0             60.0

mostly massive but with some vague bedding;

unconsolidated and soft but coherent and

competent: abruptly overlies:

UPPER EOCENE, LOWER JACKSONIAN

BARNWELL GROUP

DRY BRANCH FORMATION –    feet+

Twiggs Clay Member

Bed 2		Clay: slightly and finely sandy and silty with        31.0             64.0

increasing sand content down-section and

especially near the base of the Bed; scattered,

small grains or concretions of chert (a few

mm), more definitely cherty toward the base

of the Bed; vaguely stratified but appears to

be massive bedded; unconsolidated but tough,

very hackly fracture and the dry clay breaks

into small hackles, much of the clay was

disrupted during drilling; moderately

competent (~60% core recovery); deeply

weathered in the upper part, less weathered

below, moderate brown (5YR 3/4) in the

upper part, paling to moderate brown

(5YR 4/4) and light brown (5YR 5/4) and

dark yellowish orange (10YR 6/6) deeper in

the section, some scattered pockets of

unoxidized grayish yellow green color

(5GY 7/2); grades abruptly downward into:

Bed 3		Sand: very fine grained and well sorted,                 1.0             95.0

peculiar stuff, resembles unconsolidated

rhyolite, slightly argillaceous; structureless;

tough and competent; abruptly overlies:

Bed 4		Limestone: macrofossiliferous, very fine                  0.5             96.0

textured and cherty with scattered grains of

fine sand, probably a trace of clay minerals

but none noted; structureless; consolidated

and probably competent; abruptly overlies:

Bed 5		Clay: calcareous and finely sandy with both           4.5             96.5

interstitial sand and fine silty sand occurring

along bedding planes and partings; thinly and

finely stratified; unconsolidated but

competence is uncertain due to poor core

recovery, the clay may be competent whereas

the underlying sand may be incompetent;

the color of the clay is mostly grayish yellow

green (5GY 7/2) to pale greenish yellow

(10Y 8/2) with some yellowish gray (5Y 7/2);

overlies:

Griffins Landing Member? – 1.0 feet+

Bed 6		Sand: fine grained and well sorted, calcareous       1.0            101.0

with no other lithic component noted;

structureless; unconsolidated, soft and

probably poorly competent; overlies core gap;

bottom of the core at 113 feet.

CORE GAP	                                                                           11.0            102.0

_____________________________________

TOTAL DEPTH OF CORE – 113 FEET