Paul Huddlestun

Logged - ca. 1976

Written up – 10/29/14

WASHINGTON 12, GGS-1184

WARTHEN COUNTY, GEORGIA

Warthen 7½’ quadrangle

Approximately 4 miles north of Sandersville, Washington County,

at the jct. of Bay Springs Road and Bussell Road and

on the edge of power line clearings,

1 mile north of the of the jct. of Bay Springs Road and Linton Road

Latitude		N 33° 02.482’                            Elev. 408 Feet

Longitude        W 82° 49.773’

Lithostratigraphic

unit and bed number               Description                     Thickness          Depth  __________________________________________________________(feet)_________ (feet)

UPPER EOCENE, JACKSONIAN

BARNWELL GROUP – 105 feet+

TOBACCO ROAD SAND – 30 feet

Bed 1		Sand: massive residuum, argillaceous with           10.0              0.0

minor interstitial clay and with scattered

clay laminae; massive bedded but with some

stratification; unconsolidated, tough and

mostly competent (~80% core recovery);

weathered, sand is moderate reddish brown

(10YR 4/6) in color; grades downward into:

Bed 2		Sand: medium to coarse grained and poorly           2.0             10.0

sorted with scattered small pebbles and

granules, no other lithic components noted;

massive and structureless; unconsolidated

and poorly competent (~17% core recovery);

weathered; overlies core gap:

CORE GAP                                                                              10.0             12.0

NO CORE RECOVERY                                                               8.0             22.0

UPPER EOCENE, LOWER JACKSONIAN

BARNWELL GROUP

DRY BRANCH FORMATION – 75 feet+

Irwinton Sand Member – 65 feet

Bed 3		Clay: with thin interlayers and laminae of fine,       8.0             30.0

well sorted sand; no other lithic components;

noted; prominently layered; unconsolidated

and moderately competent (~53% core

recovery); overlies core gap:

CORE GAP                                                                                7.0             38.0

Bed 4		Sand: fine grained and well sorted; with thin,         4.0             45.0

discontinuous interlayers and laminae of clay;

thinly and prominently stratified;

unconsolidated and moderately coherent and

competent; weathered; overlies core gap:

CORE GAP                                                                                3.0             49.0

Bed 5		Sand: medium grained and well sorted; no             5.0             52.0

other lithic components noted but there is

probably a trace of clay minerals; massive and

structureless; mostly to moderately coherent

and competent (~71% core recovery); overlies

core gap:

CORE GAP                                                                                3.0             57.0

Bed 6		Clay: similar to Bed 3 but with more sand              5.0             60.0

interlayers, sand is fine grained and well

sorted, no other lithic components noted;

prominently and thinly layered;

unconsolidated but tough, resistant and

competent; grades downward into:

Bed 7		Sand: similar to Bed 4, fine grained and well          7.0             65.0

sorted sand with clay interlayers and

laminae; no other lithic components noted;                                                        prominently and thinly stratified;

unconsolidated and moderately coherent and

competent (~50% core recovery); overlies core

gaps:

CORE GAP                                                                                3.0             72.0

CORE GAP                                                                                7.0             75.0

Bed 8		Clay with sand interlayers: sand is fine grained      8.0             82.0

and well sorted; no other lithic components

noted; thickness of clay layers range from

millimeters to 2 feet, sand layers range from

millimeters to 9 inches; very conspicuously

layered; unconsolidated and competent:

grades downward into:

Bed 9		Sand: fine grained and well sorted sand with          5.0             90.0

some clay interlayers and laminae; no other

lithic components noted; prominently and

thinly stratified; unconsolidated and coherent

and competent; abruptly overlies:

Twiggs Clay Member – 10 feet+

Bed 10	Clay: scattered diatoms noted, no other                10.0             95.0

lithic components; thinly layered to

laminated; unconsolidated but tough and

coherent; bottom of the core at 105 feet.

____________________________________

TOTAL DEPTH OF CORE – 105 FEET