Paul Huddlestun

Logged - ca. 1976

Written up – 10/28/14

WASHINGTON 9, GGS-1181

WASHINGTON COUNTY, GEORGIA

Sandersville 7½’ Quadrangle

Approximately 1.6 miles west of Sun Hill and

4 miles southeast of Sandersville,

on the north side of GA 242 (Bartow Road),

immediately east of the highway and railroad crossing

in Washington County, Georgia

Latitude		N 32° 56.720’                          Elev. ~380 Feet 		Longitude		W 82° 45.362’

Lithostratigraphic

unit and bed number               Description                     Thickness          Depth  __________________________________________________________(feet)_________ (feet)

UPPER EOCENE, UPPER JACKSONIAN

BARNWELL GROUP – 75 feet+

TOBACCO ROAD SAND – 60 feet

NO CORE                                                                                   0.5              0.0

Bed 1		Cherty sand/sandy chert: sand is medium              3.0              0.5

grained and well sorted; no other lithic

components noted; structureless;

consolidated and poorly competent (~11%

core recovery); overlies:

Bed 2		Sandstone: medium grained and well sorted;           1.0              3.5

siliceous, no other lithic components noted;

structureless; well cemented but of uncertain

competence due to poor core recovery; appears

to grade downward into:

Bed 3		Sand: medium/coarse grained and moderately        4.75            4.5

well sorted; siliceous and cherty in the upper

few inches, a trace of chert below; slightly

argillaceous; mostly massive and structureless

with minor vague stratification; unconsolidated

and moderately coherent and competent (~63%

core recovery); overlies core gap:

CORE GAP	                                                                              2.75           9.25

Bed 4		Sand: medium to fine/medium grained and           2.5             12.0

well sorted; heavy MnO2 stain and somewhat

argillaceous; massive and structureless;

unconsolidated but firm, coherent and

competent (100% core recovery); deeply

weathered but pale coloration; grades

downward into:

Bed 5		Sand: medium grained and moderately sorted;       4.5             14.5

slightly argillaceous, no other lithic

components noted; massive and structureless;

unconsolidated and mostly coherent and

competent (~78% core recovery); overlies:

Bed 6		Sand:	coarse grained and poorly sorted;                  4.5             19.0           	cherty to siliceous (light color and brittleness

suggest silicification); recovered core is

structureless; partially consolidated, brittle

and poorly competent (~18% core recovery);

overlies core gap:

CORE GAP                                                                                6.5             23.5

Bed 7		Calcareous claystone/siliceous limestone:              0.5             30.0

siliceous, argillaceous, calcareous with fossil

molds, and with “limonite”-stain; structureless;                                   		dense and probably competent; abruptly

overlies:

Bed 8		Clay: calcareous with silty partings; thinly             7.0             30.5

layered, almost shaley or schist-like);

unconsolidated but very tough, almost hard

and mostly competent (~75% core recovery);                                                      grayish yellow green (5GY 7/2) in color;

overlies core gap:

CORE GAP                                                                                2.5             37.5

Bed 9		“Marl”: very calcareous and very but variably         3.0             40.0

argillaceous, variably finely sandy to silty;

some brown “limonite” stain in the upper part

of the Bed; massive and structureless

unconsolidated but tough and competent;

grades downward into:

Sandersville Limestone Member – 17 feet

Bed 10	Limestone: clayey with a trace of fine sand             3.0             43.0

and silt; clay content diminishes downward;

some scattered Turritella molds; massive and

structureless; consolidated and moderately

competent (~57% core recovery); overlies

core gap:

CORE GAP                                                                                4.0             46.0

Bed 11	Limestone: some interstitial clay and scattered       6.0             50.0

clayey layers, a trace of fine sand; massive-

bedded but vaguely and poorly layered; brittle

but not indurated, tough and with irregular

fracture; overlies core gap:

CORE GAP                                                                                4.0             56.0

UPPER EOCENE, LOWER JACKSONIAN

BARNWELL GROUP

DRY BRANCH FORMATION – 15 feet+

Bed 12	Sandstone: calcareous, no other lithic                   0.25            60.0

components noted; structureless and

indurated; abruptly overlies:

Bed 13	Clay: somewhat and variably calcareous and        4.75           60.25

with silty fine sand occurring along clay

partings; thinly stratified; unconsolidated but

tough and competent; mostly grayish yellow

green (5GY 7/2) to moderate yellow green

(5GY 7/4) in color; grades downward into:

Bed 14	Clay/sand: clay interlayered with fine sand;           5.0             65.0

sand is calcareous whereas the clay is

poorly calcareous; prominently stratified;

unconsolidated and the clay is tough, waxy

and laminated whereas the sand is soft,

loose and almost incoherent; moderately

competent (~50% core recovery); the clay

layers are grayish yellow green (5GY 7/2) in

color and the sand is almost white (N 9) in

color; overlies core gap:

CORE GAP                                                                                5.0             70.0

___________________________________

TOTAL DEPTH OF CORE – 75 FEET