Paul Huddlestun

Logged 11/8/89

Written up – 11/3/14

GEORGIA KAOLIN – CYRUS HARRIS MINE CORE, (DEEPSTEP, GA)

WASHINGTON COUNTY, GEORGIA

Deepstep 7½’ Quadrangle

Approximately 1.6 miles east of Deepstep, Washington County,

roughly 0.3 miles north of Deepstep Road,

in the Cyrus Harris mine

Latitude		~33° 00.886’                            Elev. ~248 Feet

Longitude         ~82° 56.927’

Lithostratigraphic

unit and bed number               Description                     Thickness          Depth  __________________________________________________________(feet)_________(feet)_

NO CORE                                                                                 18.0              0.0

UPPER CRETACEOUS, TAYLORAN. CAMPANIAN

OCONEE GROUP

GAILLARD FORMATION – 147 feet+

Buffalo Creek Kaolin Member – 67 feet+

Cusseta-Demopolis-equivalent

Bed 1		Kaolin: (soft kaolin) slightly micaceous; thinly        1.0             18.0

layered; unconsolidated but tough and

competent (100% core recovery); grades

downward into:

Bed 2		Kaolin: (soft kaolin) micaceous and silty; thinly      3.0             19.0

layered; unconsolidated and competent; light

gray in color; grades downward into:

Bed 3		Kaolin: slightly and finely micaceous, no              11.5             22.0

other lithic component noted; thinly layered

with ocherous coloring along bedding planes;

unconsolidated but tough and competent;

grades broadly downward into:

Bed 4		Sand: fine grained and well sorted;                       11.5             33.5

micaceous, common to abundant dark

minerals and variably kaolinitic with both

interstitial kaolin and thin layers of kaolin;

well layered; unconsolidated and moderately

coherent and competent (~52% core recovery);

grades broadly downward into:

Bed 5		Kaolin: variably silty and micaceous; thinly          14.5             45.0

layered with ocherous stain along layering;

unconsolidated and moderately competent

(~59% core recovery); light gray in color;

grades broadly downward into:

Bed 6		Kaolin: carbonaceous, micaceous and slightly        5.5             59.5

silty; thinly layered; unconsolidated and

mostly competent (~82% core recovery); light

to dark gray in color; grades broadly

downward into:

Bed 7		Kaolin: no other apparent lithic components;       20.0             65.0

laminated but appears massive bedded;

unconsolidated but tough and mostly

competent (~85% core recovery); light gray in

color: grades broadly downward into:

Gaillard Formation undifferentiated - 80 feet

Bed 8		Kaolin: (lithologically gradational between the        5.0             85.0

overlying and underlying beds) slightly silty in

the upper part, becoming more finely sandy

downward and is a clayey, fine sand in the

lower part of the Bed, no other lithic

components noted; thinly stratified with thin

sand layers in the lower part; unconsolidated

but competent; grades broadly downward

into:

Bed 9		Sand: fine grained and well sorted; kaolinitic          4.0             90.0

with both interstitial and thin layers and

laminae of kaolin, kaolin content increases

downward in the recovered core along with

an increase in clay layers and laminae; no

other lithic components noted; prominently

stratified; unconsolidated and moderately

coherent and competent (~40% core

recovery); overlies core gap:

CORE GAP                                                                                6.0             94.0

Bed 10	Sand: coarse grained and poorly sorted;              12.5            100.0

slightly kaolinitic with interstitial kaolin,

some maroon sandstone with quartz pebbles

noted at the base of the recovered core; no

other lithic components noted; rudely

stratified; unconsolidated and poorly

coherent and competent (~24% core

recovery); abruptly overlies:

Bed 11	Kaolin: slightly and finely sandy and silty,             7.5            112.5

no other lithic components noted; massive

and structureless in the upper part of the

Bed, becoming layered in the lower few feet;

unconsolidated, tough and competent;

(100% core recovery);grades downward into:

Bed 12	Sand: medium to coarse grained and                   10.0            120.0

moderately poorly sorted, less poorly sorted

in the lower few feet; kaolinitic with

interstitial kaolin and micaceous in the lower

feet, possibly somewhat feldspathic but the

feldspar appears to be degraded; mostly

massive and structureless; unconsolidated

but competent; overlies core gap:

NO CORE RECOVERY           “coarse sand cuttings”               10.0            130.0

CORE GAP                                                                               3.5            140.0

Bed 13	Sand: very coarse grained and very poorly           21.5            143.5

sorted with scattered quartz pebbles

especially in the lower part of the Bed

(some ˃1 inch in diameter), one angular,

vein quartz fragment/pebble noted;

kaolinitic with mostly interstitial kaolin but

with some scattered thin layers/laminae in

the middle part of the Bed, clay content

gradually increases down-section whereas

sorting deteriorated down-section; mostly

massive and structureless; unconsolidated

and mostly coherent and competent (~86%

core recovery); disconformably overlies:

UPPER CRETACEOUS, SANTONIAN, AUSTINIAN

OCONEE GROUP

PIO NONO FORMATION - 48 feet+

Eutaw-equivalent

Bed 14 	Sand: coarse grained and poorly sorted and          2.0            165.0

fining downward to medium to coarse and

moderately poorly sorted; kaolinitic and

clayey in texture, most of the kaolin is

interstitial; unconsolidated but tough, clayey

and moderately competent (~40% core

recovery); gray in color at the top of the Bed

becoming ocherous downward and with some       					maroon staining at the base of the recovered

Bed; overlies core gap:

CORE GAP                                                                               3.0            167.0

Bed 15	Kaolin: (top of fining upward sequence) sandy,      1.0            170.0

no other lithic component noted; massive and

structureless; unconsolidated but very tough

and competent (100% core recovery); color

mottled maroon and gray (not Gaillard gray

but Gray gray); grades downward into:

Bed 16	Sand: (lower part of fining upward sequence)       15.0            171.0

coarse grained and poorly sorted; kaolinitic

and clayey textured, with interstitial kaolin,

scattered thin layers/laminae of kaolin and

a few scattered kaolin intraclasts; no other

lithic components noted; very crudely

layered; unconsolidated but very tough and

competent; color mottled gray and maroon

above 178.5 feet, ocherous tan below 178.5

feet; grades abruptly downward into:

Bed 17	Kaolin: (top of fining upward sequence) fine           1.5            186.0

grained and well sorted, no other lithic

components noted; thinly layered;

unconsolidated but tough and competent;

color mottled deep maroon, ochre and gray;

grades downward into:

Bed 18	Sand: (middle part of fining upward sequence)      6.5            187.5

fine grained and well sorted; kaolinitic with

both interstitial kaolin and a few scattered

thin layers of kaolin; no other lithic

components noted; rudely stratified;

unconsolidated and moderately coherent

and competent (~54% core recovery);

grades downward by coarsening and

decrease in sorting into:

Bed 19	Sand: (lower part of fining upward sequence)       12.5            194.0

coarse grained, poorly sorted and pebbly;

kaolinitic and clayey textured, most kaolin is

interstitial; no other lithic components noted;

massive and structureless; unconsolidated

but very tough and competent; abruptly

overlies:

Bed 20	Kaolin: a trace of fine sand, no other lithic             6.5            206.5

components noted; mostly massive and

structureless but becoming stratified in the

basal 1 foot of the core; unconsolidated but

hard, tough, waxy and competent; color

mottled brilliant maroon and gray; bottom

of the core at 213 feet.

____________________________________

TOTAL DEPTH OF CORE – 213 FEET